## Slide 1: Fire Detection System with Customised Analog to Digital Converter and Magnitude Comparator
EEE 304 – Digital Electronics Laboratory
July 2022 Level-3 Term-II Section A1
Final Project Demonstration
Nafis Sadik
Lecturer, EEE, BUET
Mrinmoy Kundu
Lecturer(PT), EEE, BUET
Supervisors:

## Slide 3: Fire Detection System with Customised Analog to Digital Converter and Magnitude Comparator
Summary
Acknowledgement and References
Introduction
Technical Details of Design
Practical Considerations
Reflection on Individual and Teamwork
Demonstration

## Slide 4: Fire Detection System with Customised Analog to Digital Converter and Magnitude Comparator
Summary
Acknowledgement and References
Introduction
Technical Details of Design
Practical Considerations
Reflection on Individual and Teamwork
Demonstration

## Slide 5: 1. Summary / Abstract
Implemented a fire alarm using 4 bit ADC and self built magnitude comparator
An alarm will indicate the presence of fire.
Alarm will stop after certain time

## Slide 6: 2.1 Complexity Analysis
No. of components
Speed of operation
Complexity of the algorithm
Working with hardware logic gate ic

## Slide 7: Fire Detection System with Customised Analog to Digital Converter and Magnitude Comparator
Summary
Acknowledgement and References
Introduction
Technical Details of Design
Practical Considerations
Reflection on Individual and Teamwork
Demonstration

## Slide 8: 2. Introduction
21000
Fire Incidents
Reported Annually
180
People in Dhaka Dies Annually in Fire Outbreak
40%
Caused by Electrical Short Circuits

## Slide 9: Fire Detection System with Customised Analog to Digital Converter and Magnitude Comparator
Summary
Acknowledgement and References
Introduction
Technical Details of Design
Practical Considerations
Reflection on Individual and Teamwork

## Slide 10: 3.1 Design: Methods
Components
  LM35 (Temp Sensor)
  LM324 (Quad Op-Amp)
  IC7805 (5V REGULATOR)
  IC7404 (NOT)
  IC7408 (AND)
  IC7432 (OR)
  IC7486 (XOR)
  LED, BUZZER, POT
  BREADBOARD, JUMPER
  555 Timer IC

## Slide 11: 3.1 Design: Methods (Continued)
Working Range for LM35:
Temperature Limit: -50°C to 150°C
Resolution: 10mV / °C
Vmax = 1.5V
Again = 5V / 1.5V = 3.33
Temperature | Voltage | Decimal Equiv.
0-8 | 0-0.3125 | 0
8-18 | 0.3125-0.625 | 1
18-28 | 0.625-0.9375 | 2
28-38 | 0.9375-1.25 | 3
38-48 | 1.25-1.5625 | 4
48-58 | 1.5625-1.875 | 5
58-68 | 1.875-2.1875 | 6
68-78 | 2.1875-2.5 | 7
Temperature | Voltage | Decimal Equiv.
78-88 | 2.5-2.8125 | 8
88-98 | 2.8125-3.125 | 9
98-108 | 3.125-3.4375 | 10
108-118 | 3.4375-3.75 | 11
118-128 | 3.75-4.0625 | 12
128-138 | 4.0625-4.375 | 13
138-148 | 4.375-4.6875 | 14
148-150 | 4.6875-5 | 15

## Slide 12: 3.1 Design: Novelty
Implemented 4bit flash ADC using basic logic gates
Implemented 4 bit Magnitude Comparator
Simulated the working of LM35 Temperature sensor using voltage divider
Implemented a timer circuit to stop the buzzer after certain time to prevent from continuous buzzing

## Slide 13: 3.1 Design: Methods(Continued)
Temp Sensor
Output
4-bit
Flash ADC
4-bit
Magnitude
Comparator
Reference/Threshold
Temperature
(User Defined
4-bit Binary)
Tsensor < Tref
Tsensor = Tref
Tsensor > Tref
Non-Inverting
Amplifier

## Slide 14: 3.2 Design: Circuit Diagram

## Slide 15: 3.2 Design:

## Slide 16: Comparator Circuit
Comparator Boolean Expression

## Slide 17: Temperature Sensor Circuit

## Slide 18: Timer Circuit

## Slide 19: 3.3 Design: Result explanation

## Slide 21: 3.5 Implementation: Photo Gallary
16 to 4 bit ADC
4 bit Comparator
Timer Circuit

## Slide 22: Fire Detection System with Customised Analog to Digital Converter and Magnitude Comparator
Summary
Acknowledgement and References
Introduction
Technical Details of Design
Practical Considerations
Reflection on Individual and Teamwork
Demonstration

## Slide 23: 3.6 Implementation: External Links
Project Video

## Slide 24: Fire Detection System with Customised Analog to Digital Converter and Magnitude Comparator
Summary
Acknowledgement and References
Introduction
Technical Details of Design
Practical Considerations
Reflection on Individual and Teamwork
Demonstration

## Slide 25: 4. Practical Considerations: Public Health and Safety
Fire alarms play a crucial role in ensuring public health and safety by providing early warning of potential fire hazards.
Early warning: Fire alarms provide early warning of potential fires, allowing people to evacuate the building and call emergency services before the fire spreads.
Prevention: In addition to providing early warning, fire alarms can also help prevent fires from starting in the first place.
Peace of mind: Fire alarms can provide peace of mind for building occupants, knowing that they are being protected by an effective fire safety system.

## Slide 26: 4.2 Practical Considerations: Societal and Cultural
Fire alarms can have a significant impact on societal and cultural aspects in several ways.
Safety culture: Fire alarms can promote a culture of safety by raising awareness of fire hazards and encouraging individuals and organizations to take preventive measures.
Community resilience: In the event of a fire, fire alarms can help communities respond quickly and effectively to limit the impact of the fire.
Architectural design: Fire alarm reduces the probability of fire destruction of cultural heritage.

## Slide 27: 4.2 Practical Considerations: Environment
Fire alarm has significant impact on the environment.
Air pollution: Fire alarm reduces the probability of fire incidence as well as air pollution.
Habitat destruction: Fires can destroy natural habitats, leading to a loss of biodiversity and ecosystem services.
Soil contamination: Fires can result in the release of toxic substances, such as heavy metals or asbestos, which can contaminate soils and impact soil health.
Overall, fire accidents can have significant negative impacts on the environment, including air pollution, water pollution, soil contamination, habitat destruction, and climate change.

## Slide 28: Fire Detection System with Customised Analog to Digital Converter and Magnitude Comparator
Summary
Acknowledgement and References
Introduction
Technical Details of Design
Practical Considerations
Reflection on Individual and Teamwork
Demonstration

## Slide 29: 6. Reflection on Individual and Team work
6.1 Individual Contribution of Each Member
6.2 Mode of Team Work
6.3 Diversity Statement of Team
6.4 Log Book of Project Implementation

## Slide 30
Anindya Kishore Choudhury
1906081
Toki Bin Alam
1906083
Iftekar Sadiq
1906085
Ramim Hasan Shawn
1906082
Team Management

## Slide 31: 6.2 Mode of Team Work and Diversity

## Slide 32: Fire Detection System with Customised Analog to Digital Converter and Magnitude Comparator
Summary
Acknowledgement and References
Introduction
Technical Details of Design
Practical Considerations
Reflection on Individual and Teamwork
Demonstration

## Slide 33: 7. References
https://www.geeksforgeeks.org/magnitude-comparator-in-digital-logic/